## Slide 1
SPEECH ENHANCEMENT
MAXIM INTEGRATED
Stella Cao, Renjie Liu, Huaxuan Wang, Curtis Zhuang

## Slide 2
Clean speech is better
1

## Slide 3
Background
Problem Statement
Knowledge Expansion
Next Steps
Findings and Discussion
Data and Methodology
Candidate Model
Project Roadmap
2

## Slide 4
MAXIM INTEGRATED
  Technology manufacture
  MAX78000 accelerator
SPEECH ENHANCEMENT
  Improve mixed speech
  Zoom and Microsoft Teams
Working With An Analog Device Company
3

## Slide 5
Speech Enhancement Is A Harder Problem
Noise Cancellation Headphones
  Reduce ambient sounds using active noise control
Hearing Aid Requirements
  Enhance speech
  Aesthetic concern
  Power-efficient
4

## Slide 6
Huge Revenue Potential For Maxim
We developeded a speech enhancement algorithm that enables Maxim Integrated to participate in a $300 Million total addressable market.
About 28.8 million U.S. adults could benefit from using hearing aids
Max78000 priced at around $10
$300 Million
5

## Slide 7
PROBLEM STATEMENT
Develope and implement machine learning methods, compatible with Maxim Integrated's MAX78000, to enhance speech for hearing aid devices with latency less than 10ms*.
6

## Slide 8
Signal
Signal is a variation of air pressure changed over time
Recording Signals
To digitally record signals, air samples are taken over a period of time. The sampling rate commonly is 44.1k samples per second, aka 44.1k Hz
Single-Frequency Signal
In real-life, the signal consists of different single-frequency signals
Signal Is
Basic of Speech
Single-Frequency Signal Time Domain Chart
7

## Slide 9
What Is Fourier Transform
Fourier Transform
Apply the Fourier transform (FT) to decompose a signal into individual frequencies and its amplitude. But our speech's frequency content varies over time
Short-Term Fourier Transform
Short-term Fourier transform (STFT) performs Fast FT on windowed segments of the signal. The result can be visualized by Spectrogram
8

## Slide 10
Current Strategies for Speech Enhancement
Mapping-based (End to End)
(Asri et.al 2021)
  Map a non-linear function from the noisy speech into the enhanced clean speech
  Less sensitive to SNR variations
  Reconstruct the target output from the observed input
Mask-based
(Asri et.al 2021)
  Estimate a mask to filter to the input spectrogram
  Different types of mask
    Ideal binary mask (IBM)
    Ideal ratio mask (IRM)
9

## Slide 11
R-CED - CNN Model
(Park & Lee 2016)
  CNN models have lesser number of parameters and can be used in embedded devices
  CNN models has encoder and decoder structure which is suitable for generation tasks
  Can perform either mapping-based or mask-based tasks
U-Net
(Stroller, Ewert & Dixon 2018)
  U-Net strucutre is a symmetric convolutional network investigating end-to-end source separation
  The architecture's encoder captures context and the symmetric expanding path enables precise localization with its skip-connection which retains information both from the bottlenet and the convolutioned counterpart
Convolution Models Suit better than GRU and GAN for its efficiency
10

## Slide 12
White Noise
16.7%
Dog Barking
16.7%
Baby Crying
16.7%
Siren
16.7%
Engine Sounds
16.7%
Traffic Sounds
16.7%
We mixed 6 noise types with clean speech
Speech
OpenSLR LibriSpeech ASR corpus data which contains corpus of read English speech divided into train (100 hours) and validation (5 hours).
Noise (from Youtube)
Stationary:
White
Quasi-Stationary:
Siren
Non-Stationary:
Traffic, Baby crying, Dog barking, Diesel truck
11

## Slide 13
End-to-End
Speech Enhancement
PyTorch Data Pipeline Modules
Read clean speech and noise
Generate noisy speech
Apply STFT
Perform Sliding Window
Fit Speech Enhancement Model
Recover speech using ISTFT
1
2
3
4
5
6
12

## Slide 14
Feature Engineering
- Fourier Transform
Parameter of STFT:
  Window Length: 512 (32 ms)
  Number of FFT: 512
  Hop Length: 128 (8 ms)
Transform speech to magnitude (real-valued) and phase (complex-valued)
13

## Slide 15
Feature Engineering
- Sliding Window & Masking
Sliding Window:
  Fix time dimension
  Create temporal context as model inputs
Ideal Ratio Mask (IRM):
  Label of the model
  Smoothed version of IBM
14

## Slide 16
What the Basic Model Looks like
Proposed Model
  Encoder-Decoder based CNN
Objective
  Remove specific noise types
  Lightweight
Architecture
  Encoder Block:
    Conv2d, BatchNorm, Max-Pooling, and ReLU
  Decoder Block:
    TransposedConv2d, BatchNorm, and ReLU
15

## Slide 17
Hardware limitation
  Kernel Size: 3x3
  Conv2d:
    Stride: [1, 1]
    Dilation: 1
Efficient UNet-128 parameter
  5 encoder blocks
  5 decoder blocks
  Max channel size: 256
  Kernel size: 3x3
Efficient UNet-128 parameters based on MAX78000 hardware
Final Model Details
16

## Slide 18
Noise Reduction
Segmental Signal-to-Noise Ratio (segSNR)
  Signal / Noise
  Higher segSNR, lower noises
Speech Quality
Perceptual Evaluation of Speech Quality (PESQ)
  From -0.5 (bad) to 4.5 (good)
Speech Intelligibility
Short-Time Objective Intelligibility (STOI)
  From 0% (bad) to 100% (good)
How to Evaluate Speech Properly
17

## Slide 19
U-Net Stands Out
Hypothesis:
U - Net will be small enough to be embedded on Max78000 and achieve required speech enhancement performance.
  Flexible Size
  High performance architecture
18

## Slide 20
Noisy
CNN Baseline
R-CED
SimpleNet
U-Net
25
20
15
10
5
0
U-Net With Masking Performs The Best
  U-Net
    Significantly improves all 3 metrics
    Benefit from flexible of encoder-decoder architecture and skip-connection
  Mapping Method
    Unclear speech
  Masking Method
    Better performance
Train
Validation
Noise Reduction (segSNR)
19

## Slide 21
Efficient U - Net -128 Will Be Embedded
  Effective UNet-16
    The best performance
    Too large to deploy on MAX78000
  Efficient UNet
    More contextual features, better performance
  Efficient UNet -128
    Achieve similar performance with Effective UNet-16
    Small enough to embed on MAX78000
    Latency less than 3.3 ms
20

## Slide 22
White Noise
SSNR increased 8.89 dB
PESQ increased 1.01
STOI increased 6%
Baby Crying
SSNR increased 10.61 dB
PESQ increased 1.80
STOI increased 14%
Dog Barking
SSNR increased 0.32 dB
PESQ increased 0.33
STOI increased 6%
Engine Sounds
SSNR increased 10.71 dB
PESQ increased 1.25
STOI increased 8%
Traffic Sounds
SSNR increased 9.41 dB
PESQ increased 0.92
STOI increased 11%
Siren
SSNR increased 16.46 dB
PESQ increased 1.99
STOI increased 9%
Significant Improvement In Different Noise Types
PERFORMANCE ON DIFFERENT NOISE TYPES
Small UNet-128
21

## Slide 23
The model captures stationary noises well, while for non-stationary noises, the performance varies, especiallly dog bark.
Metrics may not capture all human perceivable components.
Metric Evaluation
Larger kernels, with more channels capture more features and the use of pooling layers in small models affect the upsampling process when retaining information.
Large models have small temporal context.
Model Size
Masking method has better speech intelligibility and quality as it is less prone to error caused by latency which is preferred in real-time.
Mapping vs Masking
U-Net structure allows the upsampling process to retrieve data from not only the bottleneck but retain speech resolution from the downsampling counterpart in encode-decoder.
U-Net Structure
Model Structure & Size Have Huge Impact on Performance
22
Notes: dog bark is explosive and intermittent, explosive difficult because not enough time to train
he encoder-decoder architecture extracts useful features in the encoder parts, while the decoder parts recover the corresponding target using extracted features from the encoder parts. Moreover, the long skip-connections guarantee features from the bottom of the U-Net can be flowed to the Transposed Convolution layer to recover patterns of the speech. T

## Slide 24
Our Contribution to MAX78000
High Performance
  Reduce unwanted ambient sounds using active noise control
    Average improvement by 8 times (segSNR increased by 8.96 dB)
    Latency less than 3.3 ms
Compatibility
  Adjust model to MAX78000
  Model deployment on MAX78000 is currently in progress
  High marketing potential
23

## Slide 25
Model: self learning
More noise types
Hardware
Languages
Mixed noises
Current model opens space for futher growth
Latency
24

## Slide 26
Next Steps on Speech Enhancement for MAX78000
Domain Adverserial Training
Optimize with MAX78000
Add more noise types and mix inputs
Add more languages
25

## Slide 27
Flask Demo
26

## Slide 28
zijcao@uchicago.com
STELLA CAO
renjiel@uchicago.edu
RENJIE LIU
shengyan@uchicago.edu
CURTIS ZHUANG
huaxuan@uchicago.edu
HUAXUAN WANG
Questions, comments, or suggestions?
Reach out to us!
27

## Slide 29
THANKS FOR WATCHING
Special thanks to Dr. Batuhan Gundogdu, Dr. Utku Pamuksuz,
Chris Olen and Scott Shepard for their advice and assistance in our project
28

## Slide 30
  Generate Noisy Speech(P30)
  ISTFT Model(P31)
  Ideal Ratio Mask(P32)
  Why Don't Use Phase(P33)
  Hearing Aid Future Market(P34)
  Masking and Mapping (P35)
Q & A
29
Appendix

## Slide 31
Generate Noisy Speech
  A custom PyTorch dataset module
  Total 30 conditions are considered:
    6 noise types
    5 different SNR each (-10 dB, -5 dB, 0 dB, 5 dB, 10 dB
  SNR Mixer function generate noisy speech given specific SNR value
30

## Slide 32
ISTFT Module - Recover Back to Speech Audio
  A custom module that wraps up PyTorch's istft function
  The predicted mask are multiplied with noisy magnitudes to get enhanced magnitude
  Applied transformation back (log transform, log powered transform, and quantization) on magnitude
  The istft function that has same parameter setups with stft function takes both magnitude and phase to generate enhanced speech audio
31

## Slide 33
Ideal Ratio Mask
  Ideal Binary Mask (IBM)
    Make the speech enhancement to binary classification task
  Ideal Ratio Mask (IRM)
    smoothed version of IBM
    Predicting the ratio between clean speech and noisy speech
    Widely used in SE community
  Other Masking strategies
    Take account of phase
      Complex Ideal ratio mask (cIRM)
      Phase sensitive mask (PSM)
32

## Slide 34
Why Don't Use Phase
  Phase may or may not contain useful information for Speech Enhancement task
    The unimportance of phase in speech enhancement (Wang, D., & Lim, J. , 1982)
    The importance of phase in speech enhancement (Paliwal, K., Wójcicki, K., & Shannon, B. , 2011)
  Involved complex-valued computation
    Not suitable for MAX78000 device
33

## Slide 35
Hearing Aid Future Market
34
The global “hearing aids market” size is expected to reach $11 billion by 2028, exhibiting a CAGR of 7.4 % during the forecast period.

## Slide 36
Masking vs Mapping
35
CNN and CDAE are less affected by training target and show masking and mapping approaches are approximately giving the same performance.
'The performance of masking targets was shown to be much better at high SNR for all architectures, leading to a higher variance for all the evaluation metrics than that of the mapping targets, which makes mapping targets less affected by SNR changes.' (Nossier, 2020)