## Slide 1
SPEECH ENHANCEMENT
MAXIM INTEGRATED
Stella Cao, Renjie Liu, Huaxuan Wang, Curtis Zhuang

## Slide 2
Background
Problem Statement
Knowledge Expansion
Next Steps
Findings and Discussion
Data and Methodology
Candidate Model
Project Roadmap

## Slide 3
Clean speech is better

## Slide 4
MAXIM INTEGRATED
  Technology manufacture
  MAX78000 accelerator
SPEECH ENHANCEMENT
  Improve mixed speech
  Zoom and Microsoft Teams
Working With An Analog Device Company

## Slide 5
Speech Enhancement Is A Harder Problem
Noise Cancellation Headphones
  Reduce unwanted ambient sounds using active noise control
Hearing Aid Requirements
  Enhance speech
  Aesthetic concern
  Power-efficient

## Slide 6
Huge Revenue Potential For Maxim
We developeded a speech enhancement algorithm that enables Maxim Integrated to participate in a $300 Million total addressable market.
About 28.8 million U.S. adults could benefit from using hearing aids
Max78000 priced at around $10
$300 Million

## Slide 7
PROBLEM STATEMENT
Develope and implement machine learning methods, compatible with Maxim Integrated's MAX78000, to enhance speech for hearing aid devices with latency less than 10ms.

## Slide 8
Signal
Signal is a variation of air pressure changed over time
Recording Signals
To digitally record signals, air samples are taken over a period of time. The sampling rate commonly is 44.1k samples per second, aka 44.1k Hz
Single-Frequency Signal
In real-life, the signal consists of different single-frequency signals
Signal Is
Basic of Speech
Single-Frequency Signal Time Domain Chart

## Slide 9
What Is Fourier Transform
Fourier Transform
Apply the Fourier transform (FT) to decompose a signal into individual frequencies and its amplitude. But our speech's frequency content varies over time
Short-Term Fourier Transform
Short-term Fourier transform (STFT) performs Fast FT on windowed segments of the signal. The result can be visualized by Spectrogram

## Slide 10
Current Strategies for Speech Enhancement
Mapping-based (End to End)
  Map a non-linear function from the noisy speech into the enhanced clean speech
  Less sensitive to SNR variations
  Reconstruct the target output from the observed input
Mask-based
  Estimate a mask to filter to the input spectrogram
  Different types of mask
    Ideal binary mask (IBM)
    Ideal ratio mask (IRM)
(Asri et.al 2021)

## Slide 11
R-CED - CNN Model
(Park & Lee 2016)
  CNN models have lesser number of parameters and can be used in embedded devices
  CNN models has encoder and decoder structure which is suitable for generation tasks
  Can perform either mapping-based or mask-based tasks
U-Net
(Stroller, Ewert & Dixon 2018)
  U-Net strucutre is a symmetric convolutional network investigating end-to-end source separation
  The architecture's encoder captures context and the symmetric expanding path enables precise localization with its skip-connection which retains information both from the bottlenet and the convolutioned counterpart
Convolution Models Suit better than GRU and GAN for its efficiency

## Slide 12
White Noise
16.7%
Dog Barking
16.7%
Baby Crying
16.7%
Siren
16.7%
Engine Sounds
16.7%
Traffic Sounds
16.7%
We mixed 6 noise types with clean speech
Speech
OpenSLR LibriSpeech ASR corpus data which contains corpus of read English speech divided into train (100 hours) and validation (5 hours).
Noise (from Youtube)
Stationary:
White
Quasi-Stationary:
Siren
Non-Stationary:
Traffic, Baby crying, Dog barking, Diesel truck

## Slide 13
End-to-End
Speech Enhancement
PyTorch Data Pipeline Modules
Read clean speech and noise
Generate noisy speech
Apply STFT
Perform Sliding Window
Fit Speech Enhancement Model
Recover speech using ISTFT
1
2
3
4
5
6

## Slide 14
Feature Engineering
- Fourier Transform
Parameter of STFT:
  Window Length: 512 (32 ms)
  Number of FFT: 512
  Hop Length: 128 (8 ms)
Transform speech to magnitude (real-valued) and phase (complex-valued)

## Slide 15
Feature Engineering
- Sliding Window & Masking
Sliding Window:
  Fix time dimension
  Create temporal context as model inputs
Ideal Ratio Mask (IRM):
  Label of the model
  Smoothed version of IBM

## Slide 16
What the Basic Model Looks like
Proposed Model
  Encoder-Decoder based CNN
Objective
  Remove specific noise types
  Lightweight
Architecture
  Encoder Block:
    Conv2d, BatchNorm, Max-Pooling, and ReLU
  Decoder Block:
    TransposedConv2d, BatchNorm, and ReLU

## Slide 17
Hardware limitation
  Kernel Size: 3x3
  Conv2d:
    Stride: [1, 1]
    Dilation: 1
Small UNet-128 parameter
  5 encoder blocks
  5 decoder blocks
  Max channel size: 256
  Kernel size: 3x3
Small UNet-128 parameters based on MAX78000 hardware
Final Model Details

## Slide 18
Noise Reduction
Segmental Signal-to-Noise Ratio (segSNR)
  Signal / Noise
  Higher segSNR, lower noises
Speech Quality
Perceptual Evaluation of Speech Quality (PESQ)
  From -0.5 (bad) to 4.5 (good)
Speech Intelligibility
Short-Time Objective Intelligibility (STOI)
  From 0% (bad) to 100% (good)
How to Evaluate Speech Properly

## Slide 19
Noisy
CNN Baseline
R-CED
SimpleNet
U-Net
25
20
15
10
5
0
U-Net With Masking Is The Best
  U-Net
    Significantly improves all 3 metrics
    Benefit from flexible of encoder-decoder architecture and skip-connection
  Mapping Method
    Unclear speech
  Masking Method
    Better performance
Train
Validation
Noise Reduction (segSNR)

## Slide 20
Efficient U - Net -128 Will Be Embedded
  Effective UNet-16
    The best performance
    Too large to deploy on MAX78000
  Efficient UNet
    More contextual features, better performance
  Efficient UNet -128
    Achieve similar performance with Effective UNet-16
    Small enough to embed on MAX78000
    Latency less than 3.3 ms

## Slide 21
White Noise
SSNR increased 8.89 dB
PESQ increased 1.01
STOI increased 6%
Baby Crying
SSNR increased 10.61 dB
PESQ increased 1.80
STOI increased 14%
Dog Barking
SSNR increased 0.32 dB
PESQ increased 0.33
STOI increased 6%
Engine Sounds
SSNR increased 10.71 dB
PESQ increased 1.25
STOI increased 8%
Traffic Sounds
SSNR increased 9.41 dB
PESQ increased 0.92
STOI increased 11%
Siren
SSNR increased 16.46 dB
PESQ increased 1.99
STOI increased 9%
Significant Improvement In Different Noise Types
PERFORMANCE ON DIFFERENT NOISE TYPES
Small UNet-128

## Slide 22
The model captures stationary noises well, while for non-stationary noises, the performance varies, especiallly dog bark.
Metrics may not capture all human perceivable components.
Metric Evaluation
Larger kernels, with more channels capture more features and the use of pooling layers in small models affect the upsampling process when retaining information.
Large models have small temporal context.
Model Size
Masking method has better speech intelligibility and quality as it is less prone to error caused by latency which is preferred in real-time.
Mapping vs Masking
U-Net structure allows the upsampling process to retrieve data from not only the bottleneck but retain speech resolution from the downsampling counterpart in encode-decoder.
U-Net Structure
Model Structure & Size Have Huge Impact on Performance
Notes: dog bark is explosive and intermittent, explosive difficult because not enough time to train
he encoder-decoder architecture extracts useful features in the encoder parts, while the decoder parts recover the corresponding target using extracted features from the encoder parts. Moreover, the long skip-connections guarantee features from the bottom of the U-Net can be flowed to the Transposed Convolution layer to recover patterns of the speech. T

## Slide 23
Our Contribution to MAX78000
High Performance
  Reduce unwanted ambient sounds using active noise control
    Average improvement by 8 times (segSNR increased by 8.96 dB)
    Latency less than 3.3 ms
Compatibility
  Adjust model to MAX78000
  Model deployment on MAX78000 is currently in progress

## Slide 24
Model: self learning
More noise types
Hardware
Languages
Mixed noises
Current model opens space for futher growth
Latency

## Slide 25
Next Steps on Speech Enhancement for MAX78000
Domain Adverserial Training
Optimize with MAX78000
Add more noise types and mix inputs
Add more languages

## Slide 26
Flask Demo

## Slide 27
zijcao@uchicago.com
ZIJIA(STELLA) CAO
renjiel@uchicago.edu
RENJIE LIU
shengyan@uchicago.edu
CURTIS ZHUANG
huaxuan@uchicago.edu
HUAXUAN WANG
Questions, comments, or suggestions?
Reach out to us!

## Slide 28
THANKS FOR WATCHING
Special thanks to Dr. Batuhan Gundogdu, Dr. Utku Pamuksuz,
Chris Olen and Scott Shepard for their advice and assistance in our project